## Slide 1
Jonathan Astill; NATS, UK
Veselin Stoyanov; BULATSA, Bulgaria
Prof. Dr. Frank Fichert; Worms University of Applied Sciences, Germany
“Fragmentation in the European Upper Airspace? A cost-benefit approach to harmonization.”

## Slide 2: What is “fragmentation”?
Fragmentation is defined as “the impact of having a system that has developed within the constraints both of national boundaries, and of historical decisions that may have become sub-optimal with technological or demand changes”.
Source: “The impact of fragmentation in European ATM/CNS”,
by EUROCONTROL, 2006

## Slide 3: “The impact of fragmentation in European ATM/CNS”:
“The total cost of fragmentation in ACCs and ATM systems taken together is 780 million EUR a year.”
“The transition from the existing system to an idealised, defragmented system might have prohibitive costs – indeed, achievement of such a system might be completely infeasible.”
“…25 sectors (per ACC) is a conservative assumption for a non-fragmented system.”

## Slide 4: The 3 principle issues which are labelled as being due to fragmentation are:
Disparate regulatory regimes or capabilities
Disparate – or at least non interoperable – technical systems with variable capabilities
Route network(s) and charging regimes that force airlines not to take the most direct routeings

## Slide 5: Route Network & Charging Regimes
The most economic routeing still may not necessarily be the shortest or most fuel efficient
Staff and technology costs driven by the complexity of the operations
“If the ANSPs were encouraged to price the upper air services separately from the terminal area services then the price for that service may become much more similar across Europe.”

## Slide 6: FRA is an airspace concept which is at a very advanced stage
Cross-border and inter-FAB FRA projects are real examples of defragmentation of the European airspace on a large scale.
By 2019 the FRA application is an achievement in every FAB and FABs have proven to be efficient platforms to build the defragmentation benefits in the airspace.

## Slide 7: Technical Systems & Interoperability
Updating the systems is complex due to the need to keep operations functioning 24/7
“COOPANS” - a single system already deployed with 5 ANSPs and in the process of deployment at a 6th.
iTEC and Co-Flight - both of these systems are on the verge of deployment and will bring the technical systems across Europe to a level of capability superiority

## Slide 8: Regulatory Regimes
Complex regulatory frameworks with highly interdependent set of SES & EASA regulations
Member States should all agree to set aside national regulatory and cultural frameworks

## Slide 9: “A proposal for the future architecture of the European airspace”
Launch airspace re-configuration supported by an operational excellence programme to achieve quick wins
Realise the de-fragmentation of European skies through virtualisation and the free flow of data among trusted users across borders
Create a legal and financial framework that rewards early movers

## Slide 10: “A proposal for the future architecture of the European airspace”
Digital technology and ATM Data Service Providers will be able to create a cloud-type service layer
The choice for the customers of ATM will be greater, much more efficient and transparent as to the number of fragments from which it is comprised
De-fragmentation here is supposed to be achieved by the availability of these “fragments” but acting in an absolutely different way

## Slide 11: Economic aspects of (de-)fragmentation
Operational level to be analysed: - ANSP - ACC - Sector
Indicators: - Productivity => Output / Input (partial vs. total – either incomplete or aggregation necessary) - Cost efficiency => Cost / Output (aggregation of outputs necessary – e.g. Composite Flight Hours, CFH)

## Slide 12: Economic aspects of (de-)fragmentation
Size and layout of operational units: Potential productivity increase
ANSP ‚A‘
ANSP ‚B‘
Merging sectors in low traffic periods
ANSP ‚A‘
ANSP ‚B‘
Cross border design of sectors according to traffic flows

## Slide 13: Economic aspects of (de-)fragmentation
Staff flexibility (e.g., on average less ‘backup’ needed with increasing number of staff which might perform the same tasks – similar to airlines’ fleet homogeneity)
Overhead functions (usually showing ‘economies of scale’)
‘Countervailing power’ (purchasing equipment – cost efficiency increases)
Complexity of larger units (X-Inefficiency – ‘diseconomies of scale’ – US example)

## Slide 14: Options to overcome fragmentation
Cooperation | Concentration (‚Mergers‘)
Limited potential (in particular operational cooperation) Joint procurement difficult (see example strategic airline alliances) | Always ‘cross-border’ merger Larger benefits (compared to cooperation) only if also consolidations of operational units (e.g. ACCs) and/or headquarters – differences in personnel costs matter – Political feasibility?
In general:
Optimum structure changes over time (due to changing traffic flows and changing technology)
Path dependency (with high share of irreversible investment – including staff training)

## Slide 15: Conclusions
“Fragmentation” must be clearly defined if this term will play a role for policy purposes
FRA is the ultimate tool to remove the airspace fragmentation but disparate regulation, charging and technology are in the way
The Airspace Architecture proposal aims to explore new avenues by means of innovative data services